## Slide 1: ENG1003 Freshman Seminar for Engineering AAE Design of Path Planning Algorithm for Aircraft Operation Week 4: Path Planning Algorithm and Python Robotics
Dr Li-Ta Hsu and Dr Weisong Wen
Assisted by
Man Hei CHENG (Melvin), Miss Hiu Yi HO (Queenie), Miss Yan Tung LEUNG (Nikki)

## Slide 2: A* Path Planning Algorithm

## Slide 3: Definition of Path Planning
Start node
1 meter for one grid
Goal node
Search Space — A collection of nodes, like all board positions of a board game.
Node — All potential position you can go across with a unique position
Gobang
Objective of path planning— Find the shortest routes with smallest cost from start node to goal node.
Route 1
Route 2
How to find the shortest route!

## Slide 4: Path Planning using A Star Method
Start node
1 meter for one grid
Goal node
8 neighboring node and the cost can be calculated as follows!
Definition of cost:
— this represents the exact cost of the path from the starting node to node
— this represents the heuristic estimated cost from node to the goal node.
—cost of the neighboring node
Node 1:
=6.8 meters
with meter and
Node 1
5 meters
3 meters
=5.8 meters

## Slide 5: Path Planning using A Star Method
Start node
1 meter for one grid
Goal node
8 neighboring node and the cost can be calculated as follows!
Definition of cost:
— this represents the exact cost of the path from the starting node to node
— this represents the heuristic estimated cost from node to the goal node.
—cost of the neighboring node
Node 2:
=6.79 meters
with meter and
Node 2
5 meters
2 meters
=5.38 meters

## Slide 6: Path Planning using A Star Method
Start node
1 meter for one grid
Goal node
8 neighboring node and the cost can be calculated as follows!
Definition of cost:
— this represents the exact cost of the path from the starting node to node
— this represents the heuristic estimated cost from node to the goal node.
—cost of the neighboring node
Node 3:
=7.32 meters
with meter and
Node 3
6 meters
2 meters
=6.32 meters
Similar cost calculation method for other 5 nodes

## Slide 7: Path Planning using A Star Method
Node | 1 |  |  |  |  |  |  | 
 | 1 | 1.414 | 1 | 1.414 | 1 | 1.414 | 1 | 1.414
 | 5.8 | 5.38 | 6.32 | 7.28 | 7.62 | 8.06 | 7.21 | 6.40
 | 6.8 | 6.79 | 7.32 | 8.694 | 8.62 | 9.474 | 8.21 | 7.814
 | 1 | 1.414 | 1 | 1.414 | 1 | 1.414 | 1 | 1.414
 | 5.8 | 5.38 | 6.32 | 7.28 | 7.62 | 8.06 | 7.21 | 6.40
 | 6.8 | 6.79 | 7.32 | 8.694 | 8.62 | 9.474 | 8.21 | 7.814
Start node
1 meter for one grid
Goal node
Definition of cost:
— this represents the exact cost of the path from the starting node to node
— this represents the heuristic estimated cost from node to the goal node.
—cost of the neighboring node
Node 1
5 meters
3 meters
=5.8 meters

## Slide 8: Path Planning using A Star Method
Start node
1 meter for one grid
Goal node
8 neighboring node and the cost can be calculated as follows!
Definition of cost:
— this represents the exact cost of the path from the starting node to node
— this represents the heuristic estimated cost from node to the goal node.
—cost of the neighboring node
Node 2 leads to smallest cost
Node 2

## Slide 9: Calculate the cost of node
Start node
1 meter for one grid
Goal node
8 neighboring node and the cost can be calculated as follows!
Definition of cost:
— this represents the exact cost of the path from the starting node to node
— this represents the heuristic estimated cost from node to the goal node.
—cost of the neighboring node
Search from the neighbouring node with smallest cost until reaching the goal!
Shortest Trajectory

## Slide 10: A star method example
destination
Wall (obstacles) cannot be touched!
Source: PythonRobotics
Each time A* enters a node, it calculates the cost, f(n)(n being the neighboring node), to travel to all of the neighboring nodes, and then enters the node with the lowest value of f(n).
These values we calculate using the following formula:
https://towardsdatascience.com/a-star-a-search-algorithm-eb495fb156bb
Shortest Trajectory

## Slide 11: Code: set up start and goal node
Start node
Goal node
Set up the start and goal nodes using the code
Start node
Goal node

## Slide 12: Code: set up obstacle
Start node
Goal node
Set up the obstacle using the code
Obstacle (wall)

## Slide 13: Code: neighboring node search
Start node
Goal node
neighboring node search
Obstacle (wall)

## Slide 14: Code: cost calculation
Heuristic cost calculation
exact cost calculation

## Slide 15: Code: calculation of final path

## Slide 16: Additional Cost.

## Slide 17: Flight planning considering trip cost
Can we consider this cost to our path planning to imitate the path planning for flights?
The fundamental rationale of the cost index concept is to achieve minimum trip cost by means of a trade-off between operating costs per hour and incremental fuel burn.
With
  =cost of fuel per kg
  =time related cost per minute of flight
  =fixed cost independent of time
  =time related cost per minute of flight
  =trip fuel (e.g. 3000kg/h)
  =trip Time (e.g. 8 hours from Hong Kong to Paris)

## Slide 18: Flight planning considering trip cost
Fuel-consuming area: the volume of fuel consumption is twice larger than other area duet to unstable airflow. (additional cost )
Time-consuming area: the flying speed is limited due to the air traffic control. (additional cost )
Start node
One white grid with cost as follows for :
Goal node
Cost can be calculated using the following formula:
One colored grid with cost as follows for:

## Slide 19: How we choose the routes ?
Fuel-consuming area: the volume of fuel consumption is twice larger than other area duet to unstable airflow. (additional cost )
Time-consuming area: the flying speed is limited due to the air traffic control. (additional cost )
Start node
Goal node
?
?
It depends on the and
One white grid with cost as follows for :
Cost can be calculated using the following formula:
One colored grid with cost as follows for:

## Slide 20: Example route planning
Avoiding the Fuel-consuming and time-consuming area if their cost is too high?
Fuel-consuming area
Time-consuming area
Trajectory

## Slide 21: Example route planning
Go through the fuel-consuming and time-consuming area if their additional cost is quite small?

## Slide 22: Design your route
Aircraft Model |  |  |  |  |  |  | 
PolyU-A380 | 1 | 1 | 2 | 5 | 10 | 0.2 | 0.2
PolyU-A381 | 1 | 1.5 | 3 | 5 | 10 | 0.3 | 0.4
PolyU-A382 | 1 | 2.0 | 4 | 5 | 10 | 0.4 | 0.5
PolyU-A383 | 1 | 2.5 | 5 | 5 | 10 | 0.5 | 0.1
Aircraft Model |  |  |  |  |  |  | 
PolyU-A380 | 1 | 1 | 2 | 5 | 10 | 0.2 | 0.2
PolyU-A381 | 1 | 1.5 | 3 | 5 | 10 | 0.3 | 0.4
PolyU-A382 | 1 | 2.0 | 4 | 5 | 10 | 0.4 | 0.5
PolyU-A383 | 1 | 2.5 | 5 | 5 | 10 | 0.5 | 0.1
With
  =cost of fuel per kg
  =time related cost per minute of flight
  =fixed cost independent of time
  =time related cost per minute of flight
  =trip fuel (e.g. 3000kg/h)
  =trip Time (e.g. 8 hours from Hong Kong to Paris)